# Decibel Exposure Time Guidelines

Accepted standards for recommended permissible exposure time for continuous time weighted average noise, according to NIOSH (National Institute for Occupational Safety and Health) and CDC (Centers for Disease Control and Prevention) in 2002.

For every 3 dBs over 85dB, the permissible exposure time before possible damage can occur is cut in half.

Continuous dB	Permissible Exposure Time

85 db	8 hours

88 dB	4 hours

91 db	2 hours

94 db	1 hour

97 db	30 minutes

100 db	15 minutes

103 db	7.5 minutes

106 dB	3.75 minutes

109 dB	1.875 minutes

112 dB	0.9 minute

115 dB	0.5 minute

vs.

From OSHA website:

| Continuous db A-weighted | Hours |
| --- | --- |

85	16

88	10.6

91	7

94	4.6

97	3

100	2

103	1.3

106	0.9   (52 minutes)

109	0.6   (34 minutes)

112	0.4   (23 minutes)

115	0.25  (15 minutes)

118	0.16  (9.6 minutes)

121	0.11  (6.6 minutes)